## Slide 1: Use of Steam to Enhance VOC-TPH NAPL Mixture Dissolution at a Major Source Area through Volatilization, Recovery, and Biodegradation Naval Air Station North Island, San Diego, CA
Vitthal Hosangadi, Pamela Chang, Michael Pound, Michael Price

## Slide 2: Project Team
Michael Pound
Michael Pound
Vitthal Hosangadi, PE*
Pamela Chang
Michael Price
* Presenting

## Slide 3: Presentation Overview
Background
Site Conditions
Objectives
Results
Key Findings (To Date)

## Slide 4
1. Background
Building 379 has a footprint of 172,000 square feet and partially overlies a LNAPL plume
Groundwater is at 23 feet bgs
LNAPL is present below the building
Elevated levels of cVOCs and TPH are present in sub-slab soil gas
Indoor air was above screening levels
A Time Critical Removal Action was implemented to mitigate indoor air

## Slide 5
1.1 Site Conceptual Model
Building 379

## Slide 6: 1.2 B379 Conceptual Site Model
172,000 SF
LNAPL at 23’ bgs
LNAPL includes:
98% TPH : JP-5, Stoddard Solvent
2%: cVOCs - TCE, 1,1,1-TCA
Base Steam Line
Elevated VOCs in Sub-Slab Soil Gas
Elevated VOCs in Indoor Air
The heat from the steam pipe has radiated through the soil (~20 feet vertically)
Laterally, increased temperatures are observed at least 30 feet away from the steam pipe

## Slide 7
2.0 Site Conditions
Volatilization of the LNAPL has resulted in soil vapor concentrations >10,000,000 µg/m3 (likely exacerbated by the elevated LNAPL temperatures)
cVOCs represent approximately 50% of the soil vapor concentrations (although < 2% of LNAPL is cVOCs)
cVOCs are the main risk driver (specifically TCE) and are present in sub-slab soil vapor at several orders of magnitude above project screening levels
Elevated TCE concentrations in sub-slab soil gas caused TCE concentrations in indoor air to exceed action levels, resulting in relocation being offered to some personnel

## Slide 8
2.1 Site Conditions - LNAPL Extent over Time

## Slide 9
2.2 Site Conditions - LNAPL/GW Temperatures (2018)
TPH -LNAPL
TCE - LNAPL
STEAM LINE

## Slide 10
2.3 Site Condition - Remedial Activities 2016
A soil vapor extraction (SVE) system has been in operation since May 2016, consisting of:
  Two horizontal SVE wells under the northern portion of the building at 10 feet bgs
  A vapor extraction and treatment system that uses compression and refrigeration to condense the TPH/cVOCs in extracted vapor to liquid product
The SVE system was installed as a VI mitigation measure, coupled with sealing 15,000 feet of cracks and joints in the floor

## Slide 11
3.0 Objective
Present an overview of a complex remedial approach at Building 379, Naval Air Station North Island (NASNI) in San Diego, CA, including:
SVE using horizontal wells under Building 379 to extract soil vapor with elevated levels of total petroleum hydrocarbons (TPH) and chlorinated volatile organic compounds (cVOCs)
Volatilization of light non-aqueous phase liquid (LNAPL) with SVE
Biodegradation of TCE in LNAPL
Enhancement of volatilization and biodegradation by injecting steam under LNAPL

## Slide 12
4.1 Effect of SVE on cVOCs in LNAPL
SVE operation has removed 17,000 lbs (2,100 gallons) of TPH/cVOCs from soil gas between May 2016 and April 2018
Significant decrease in cVOCs in LNAPL due to SVE (Note – the SVE wells are ~ 13 feet above the top of LNAPL)
Decreases in LNAPL thickness were also observed
cVOCs in extracted vapor at 50% (same as TPH), vs. 2% within LNAPL (vs. 98% TPH)
cVOCs are decreasing within LNAPL at a much greater rate than TPH (approximately 50 times faster)

## Slide 13
4.2 Degradation of TCE in LNAPL
Significant levels of cDCE were detected in soil vapor, both in sub-slab and at depth – this is most likely due to biodegradation of TCE
There is ample electron donor (TPH in the jet fuel and Stoddard Solvent)
Biodegradation of TCE in LNAPL was confirmed in bench-scale treatability tests (unamended controls showed a decrease in TCE coupled with an increase in cDCE)
Currently, levels of cDCE>TCE in soil vapor probes that are close to the Base steam line, whereas TCE>cDCE away from steam line

## Slide 14
4.3 Effect of Steam on Degradation of TCE in LNAPL
VMP-11D is ~15 feet from Steam Line: DCE>TCE
VMP-5A is ~100 feet from Steam Line: TCE>DCE

## Slide 15
4.4 Steam: Friend or Foe?
Based on this, instead of mitigating the effects of steam, it was decided to add more steam to the subsurface!
Initially, steam was considered to be a foe:
Increased temperatures of LNAPL – likely exacerbated levels of VOCs in sub-slab soil vapor
Response was to consider engineering measures to mitigate
But then, the following were considered:
The LNAPL footprint has shrunk in past few years, concurrent with increase in LNAPL temperatures
cDCE within LNAPL has increased significantly, coupled with a decrease in TCE – likely due to biodegradation of TCE, which may have been caused or enhanced by the elevated temperatures
The SVE wells are effectively capturing cVOCs/TPH from sub-slab soil gas and decreasing LNAPL mass

## Slide 16
TPH -LNAPL
TCE - LNAPL
4.5 Remedial Activities 2017
SVE Wells
Steam Injection Wells
NAPL Recovery Wells
Two horizontal SVE wells in the southern portion of the building at 10 feet bgs
One horizontal SVE well in the northern portion of the building at 20 feet bgs
Three steam injection wells (screened 5 feet below LNAPL) to enhance LNAPL volatilization and biodegradation
Two horizontal LNAPL recovery wells (screened just below the LNAPL) to recover mobilized LNAPL (due to steam injection)

## Slide 17
Steam Injection Manifold
Horizontal Well – The Beginning.......
…..The End (A few days later)
The Project Team – Some of them are here today
4.6 Remedial Activities 2017

## Slide 18
4.7 Steam Injection
Steam is being injected into the aquifer through the steam injection wells to further heat up the groundwater and the LNAPL above it (injection started 06 February 2018)
Steam injection testing ongoing
  Approximately 3,000 lbs/hr at 15 psig
  Started with few hours/day, followed by 3 days continuous
  Temperature increases of up to 30 oF were observed in product after 50 hours of injection
Evaluation of effect of steam injection on concentrations in extracted vapor is ongoing
Steam injection is expected to decrease the viscosity of the LNAPL and facilitate extraction via the LNAPL recovery wells

## Slide 19
4.8 Effect of Steam Injection
No. | Parameter | Before Steam Injection | After Steam Injection
1 | VOC Reading (PID): SVE-1B Influent | 1,500 ppm | 4,200 ppm
2 | VOC Reading (PID): SVE-3 Influent | 130 ppm | 520 ppm
3 | Temperature of Extracted Vapor | 70 ºF | 85 ºF
4 | Volume of Effluent of C3 System | 20 gallons | 40 gallons
Steam injection has significantly increased the rate of recovery of contaminants from the subsurface

## Slide 20: 4.9 Temperature Increases in LNAPL with Steam Injection
Chart: Temperature Increases in Temperature Monitoring Wells
| PW-66 | PW-68 | PW-69 | PW-70 | PW-71 | MW-07
AMBIENT | 78.5 | 76 | 79.7 | 76.2 | 76.8 | 82.8
INJECTING | 96.9 | 79.5 | 76.5 | 81.3 | 83.7
INJECTING- DAY 2 NON-CONTINUOUS | 78.9 | 74.6 | 86.2
OFF- 2 WEEKS POST INJECTION | 100.2 | 79.8 | 76.3 | 76.7
AFTER 3 DAY INJECTION | 80.6 | 120 | 82 | 77.1 | 78.2 | 83.3

## Slide 21
5.0 Key Findings (To Date)
QUESTIONS?
SVE coupled with sealing of cracks/joints has caused indoor air TCE to be < IASL
Levels of cVOCs in sub-slab soil gas (while SVE is on) are orders of magnitude below baseline; operation of 2 wells in the northern portion was adequate to decrease indoor air cVOCs to acceptable levels
SVE is remediating LNAPL:
  Over 2,100 gallons of TPH/cVOCs have been recovered as of April 2018
  Levels of cVOCs in LNAPL have decreased significantly since SVE was started, even though the SVE wells are screened 13 feet above the top of LNAPL
  Levels of cVOCs in LNAPL are decreasing about 50 times faster than TPH
The Base steam line (6 feet bgs) is heating up the LNAPL (23 feet bgs) to over 100 ºF, TCE in the LNAPL is biodegrading to cDCE, either caused or enhanced by the steam
Steam injection (to date) has resulted in tripling of SVE influent levels, and doubling of liquid volumes in effluent of the C3 system